Sony IPS-3000 GPS string before memory reset 17/9/2000-09-17

SONY110009170090607s3527195E14906184+06820110239807072061946Q4AACaACCEmABFDCACQGMABeGHABuFHACWGiABgDnABPDDAE

SONY11	Sony GPS Receiver Version 1.1

0009170090607	Time Sun 17/9/2000 9:06:07 UTC

s3527195	35 deg 27' 19.5" South (not current)

E14906184	149 deg 6' 18.4" East

+0682		Altitude 682 m

011		Velocity 11 kmph

023		Bearing 23 degrees

9807072061946	Calc Time Tue 7/7/98 6:19:46 UTC

Q		DOP 100+

4		4 Satellites

A		WGS84

ACaAC		Rx ch 1

CEmAB		Rx ch 2

FDCAC		Rx ch 3

QGMAB	Rx ch 4

eGHAB		Rx ch 5

uFHAC		Rx ch 6

WGiAB		Rx ch 7

gDnAB		Rx ch 8

P		Clock Difference

DD		Unknown

A		Degree Minutes Seconds Mode

E		Even Parity

CN1 connects to RF board

CN2 is for TTL data out, CN3 is for RS232 data out

Pin 1 is V+  +8v				DB9 Pin 9

Pin 2 is Ground				DB9 Pin 4

Pin 3 is 					DB9 Pin 8

Pin 4 is Data to GPS Rx			DB9 Pin 3

Pin 5 is Data from GPS Tx		DB9 Pin 7

Pin 6 is Data Request In RTS		DB9 Pin 2

Pin 7 is 					DB9 Pin 6

Pin 8 is Reset Active low (gnd)	DB9 Pin 1

Db9 Pin 5 is not present

S1 pushbutton is the reset button

The Baud rate is controlled by dip switch S2 on the data board

BS1 BS0 Baud Rate

0   0   9600	Default

0   1   4800

1   0   2400

1   1   1200

GPS   Terminal

2 <--- 8,7	RTS/CTS

3 <--- 3		TxD

4 ---- 5		Gnd

7 ---> 2		RxD

9 <--- 		+8 Volts

1,4	DTR/DSR